## Slide 1: SRS Timing Jitter: More Clarity
Michael Phipps

## Slide 2: Direct measurement of 25/Sqrt(12) Effect … But What Else?
NIM Trg In
SRS
Trg Out
Sqrt(12)
Trigger on Trg In on scope
Measure SRS Trigger Jitter

## Slide 3
Use Function Generator to Go In and Out of Phase with SRS
“In phase” External Pulser
“Out of phase” External Pulser
Mean time of waveform
SRS
Internal Pulser
In Phase
External
Pulser
Out of
Phase
External Pulser
Note:
SRS clock not exactly 40 MHz
Pulser and SRS clocks drift over time
Cannot be perfectly in phase w/o synching clocks
25 ns
Ratio of 2 Peaks:
1:1.79

## Slide 4
Waveforms from the two timing peaks
Peak 1
Peak 2
Same pulse shifted in time
Discreteness is visible in raw data plots

## Slide 5
Internal Pulser Data
Mean Time of Channel 1
Mean Time of Channel 2
Residual Mean Time of
Two Channels
Measurement Error (pedestals, etc)
Accounts for width of each peak but not discreteness.

## Slide 6
In Phase (sigma = 0.97 ns) External Pulser Data
Mean Time of Channel 1
Mean Time of Channel 2
Residual Mean Time of Two Channels
Measurement Error
(pedestals, etc)

## Slide 7
Out Of Phase (sigma = 6.33 ns) External Pulser Data
Mean Time of Channel 1
Mean Time of Channel 2
Residual Mean Time of Two Channels
Measurement Error
(pedestals, etc)

## Slide 8
What it Isn’t
What it Is (or might be)
Not dependent on width of discriminated NIM pulse
Not caused by any ringing on our end
Not dependent on test setup. Present when we directly inject on strips as well as normal GEM operation
Not dependent on relative location within time bin. Same distribution for 5, 10, 15, … ns delay between external pulser channels
Caused by something in external trigger pipeline – discreteness not there for internal pulser triggered data but is for in phase external pulser triggered data
Smaller (trigger) peak comes first in ratio of 1:1.79
~25 ns apart. One clock cycle.
Discreteness is visible by eye in raw data plots. Obvious 1 time bin shift in line with 1:1.79 ratio.
Present for random as well as cyclic (function generator) triggers. Random triggers have full sqrt(12) effect convoluted in data, while cyclic triggers have < sqrt(12) convoluted
Ringing effect within FEC/SRS?
Bug in early version of FEC/APV? Our FEC/APVs are older versions. Have not tested on newer versions. Does anyone else see the same thing?